## Slide 1: PREPARING TO LOAD SINGLE CARGO
2023

## Slide 2
We are preparing to load cargo of Kerosene. All cargo tanks and slop tanks are inerted. Please go to the "CCR - Mooring and Checklist" and make sure the ship is moored port side, in position and ready to receive terminal personnel.

## Slide 3
Specify mooring position „port side“ to the terminal pier.

## Slide 4
Make sure the ship is moored port side, in position and ready to receive terminal personnel.

## Slide 5
Fill in the Pre-Transfer Checklist with the Terminal Staff

## Slide 6
The Terminal has indicated that the checklist is complete.
On "SYS - Cargo Handling System" page and remove the blanks from manifolds #3 and #4 portside.

## Slide 7
1
2
3
Click at the manifold CT3 to bring up the popup window, and in that window press yellow button "BLANK" and it will turn grey.

## Slide 8
Click at the manifold CT4 and repeat

## Slide 9
Check the condition of manifolds #3 and #4 portside – are the blanks off

## Slide 10
On "SYS - Cargo Handling System" page select manifolds CT3, CT4 and change status to „Connect“.

## Slide 14
Back to "CCR - Manifolds state" and ask the terminal to prepare loading arms for loading.
(for manifolds "CT3P CT3S" and "CT4P CT4S" select Manifold State "Loading")

## Slide 17
For CT3P CT3S manifold select Manifold State "Loading", then select Cargo Type "Kerosene" and then set Cargo Flow to 200 m3/h.

## Slide 18
For CT4P CT4S manifold select Manifold State "Loading", then select Cargo Type "Kerosene" and then set Cargo Flow to 200 m3/h.

## Slide 20
To prepare cargo system for loading single cargo, proceed to "SYS - Cargo Handling System" and open all crossover valves between cargo lines:
CV20, CV21, CV22, CV23, CV24 and CV202, CV212, CV222, CV232, CV242

## Slide 21
For open valves on drop line of cargo tanks # 3 P/S, you need to open valves on dropline in cargo tanks # 3 P/S. We are going to start loading into these tanks. Go back to the "CMS - Computerized Monitoring System - Cargo System" and open valves CV06P and CV06S.

## Slide 22
Open valves CV06P and CV06S. System is prepared. You need to inform shore terminal staff that we are ready for loading

## Slide 23
Terminal representative confirmed that they are also ready for loading and we can open manifold valves.
Go to "CMS - Computerized Monitoring System - Cargo System" and open manifold valves CV15P and CV14P

## Slide 24
Loading to cargo tank #3 has being started.

## Slide 25
Open valves on drop lines for all other cargo tanks, except Slop Tanks.
Go to "CMS - Computerized Monitoring System - Cargo System" and open valves CV10P, CV08P, CV04P, CV02P, CV02S, CV04S, CV08S, CV10S)

## Slide 26
Cargo is going into the all tanks. Check the level of ullage in tanks!

## Slide 27
We need to do is to increase loading rate of loading to the maximum.
Go back to "CCR - Manifolds state" and set Cargo Flow to 1000 m3/h for the manifolds #3 and #4.

## Slide 28
We need to start discharging the ballast water by gravity. Go to "CMS - Ballast System" and open the following valves:
COL V, F/P, BT1P, BT1S, BT2P, BT2S, BT3P, BT3S, BT4P, BT4S, BT5P, BT5S, INTERCON, BV3P, BV3S, BV2P, BV2S, SUCT1 and SUCT2.

## Slide 29
Check the conditions - ballast is discharging by gravity!

## Slide 30
Check the conditions - ballast is discharging by gravity!

## Slide 32
Check the conditions - Cargo is loading into all cargo tanks. Ullages in tanks are reducing.

## Slide 33
Check the conditions – single cargo “Kerosene” is loading into all cargo tanks. We can observe the level of vapour, the concentration of nitrogen, oxygen, and CO2